## Slide 1: Quality management THE SHEWHART CONTROL CARDS

## Slide 2
.
Data for the Exercise:
From a production process, 10 samples were taken. Each sample contains 5 measurements of a quality characteristic (e.g., part length in mm):
Sample | Measure 1 | Measure 2 | Measure 3 | Measure 4 | Measure 5 | Mean (X̄) | Range (R)
1.0 | 10.1 | 10.3 | 10.4 | 10.2 | 10.2 |  | 
2.0 | 10.2 | 10.3 | 10.1 | 10.3 | 10.4 |  | 
3.0 | 10.3 | 10.4 | 10.3 | 10.5 | 10.2 |  | 
4.0 | 10.1 | 10.2 | 10.2 | 10.3 | 10.4 |  | 
5.0 | 10.3 | 10.4 | 10.2 | 10.3 | 10.5 |  | 
6.0 | 10.0 | 10.1 | 10.2 | 10.1 | 10.0 |  | 
7.0 | 10.2 | 10.1 | 10.3 | 10.2 | 10.1 |  | 
8.0 | 10.3 | 10.2 | 10.2 | 10.4 | 10.3 |  | 
9.0 | 10.4 | 10.3 | 10.5 | 10.4 | 10.6 |  | 
10.0 | 10.2 | 10.3 | 10.2 | 10.1 | 10.2 |  | 

## Slide 3
.
For each sample, calculate:
The sample mean (X̄)
The range (R) = maximum value − minimum value
2. Calculate overall statistics:
- Average of all sample means → X̄̄
- Average of all sample ranges → R̄
3. Use the following control chart constants for n = 5:
- A₂ = 0.577
- D₃ = 0
- D₄ = 2.115
4. Calculate control limits:
For the X̄ chart:
- UCL = X̄̄ + A₂ × R̄
- CL = X̄̄
- LCL = X̄̄ − A₂ × R̄
- For the R chart:
- UCL = D₄ × R̄
- CL = R̄
- LCL = D₃ × R̄
5. Plot two control charts:
- One for sample means (X̄ chart)
- One for sample ranges (R chart)
6. Interpret the charts:
- Is the process statistically controlled?
- Are there any points outside the control limits?
- Do you observe any unusual patterns (e.g., trends, cycles)?

## Slide 4
.
Sample | Measure 1 | Measure 2 | Measure 3 | Measure 4 | Measure 5 | Mean (X̄) | Range (R)
1,0 | 10,1 | 10,3 | 10,4 | 10,2 | 10,2 | 10,24 | 0,30
2,0 | 10,2 | 10,3 | 10,1 | 10,3 | 10,4 | 10,26 | 0,30
3,0 | 10,3 | 10,4 | 10,3 | 10,5 | 10,2 | 10,34 | 0,30
4,0 | 10,1 | 10,2 | 10,2 | 10,3 | 10,4 | 10,24 | 0,30
5,0 | 10,3 | 10,4 | 10,2 | 10,3 | 10,5 | 10,34 | 0,30
6,0 | 10,0 | 10,1 | 10,2 | 10,1 | 10,0 | 10,08 | 0,20
7,0 | 10,2 | 10,1 | 10,3 | 10,2 | 10,1 | 10,18 | 0,20
8,0 | 10,3 | 10,2 | 10,2 | 10,4 | 10,3 | 10,28 | 0,20
9,0 | 10,4 | 10,3 | 10,5 | 10,4 | 10,6 | 10,44 | 0,30
10,0 | 10,2 | 10,3 | 10,2 | 10,1 | 10,2 | 10,20 | 0,20

## Slide 5
.
X̄ Chart:
X̄̄ = 10.268
R̄ = 0.26
A₂ = 0.577
Upper Control Limit (UCL) = X̄̄ + A₂ × R̄ = 10.268 + 0.577 × 0.26 = 10.418
Center Line (CL) = X̄̄ = 10.268
Lower Control Limit (LCL) = X̄̄ − A₂ × R̄ = 10.268 − 0.577 × 0.26 = 10.118
R Chart:
R̄ = 0.26
D₄ = 2.115
D₃ = 0
Upper Control Limit (UCL) = D₄ × R̄ = 2.115 × 0.26 = 0.550
Center Line (CL) = R̄ = 0.26
Lower Control Limit (LCL) = D₃ × R̄ = 0 × 0.26 = 0.000

## Slide 6
.